## Slide 1: ME2 — Hey Delta Wakeword Model
Always-on “Hey Delta” detection on the Pi · fully offline
3 October 2026 · Arvir Jane R. Redondo · Model · Training on A100 · Validation on Raspberry Pi 5
Model
Mic · 16 kHz → log-mel 40 × 147 (1.5 s, every 100 ms)
BC-ResNet-6 encoder × 12 blocks · 96 → 192 channels
frequency (2-D) + temporal (1-D) branches · dilation 1, 2, 4, 8
Wake head · 1 logit → sigmoid
Fires: 2 of 3 windows ≥ 0.7335
Chime → command capture
Raspberry Pi 5 · 4 GB
Item | Value
Parameters / weights | 0.19 M (185,689) · 2.0 MB fp32 ONNX
Validation on the Raspberry Pi 5
Item | Value
Wake detect / false wake | 100% (202 of 202) / 0 of 16
Held-out test | real Pi 33/33 · new TTS voices 86% · FPR ≤ 0.16%
Latency / RTF | 4.8 ms per 1.5 s window (server core) / 0.003
Runtime | onnxruntime · 1 thread · fp32
What made the difference
Change | Effect
+405 TTS voices (train had 5) | Unseen voices detected: 63% → 91%. The model had memorised the 5 voices.
Noise over the whole window | “Hey + word” false accepts: 3.7% → 0.07%. Quiet padding had become a shortcut cue.
Hard-negative mining | Did not help: 17.3 vs 6.2 false accepts per hour, so it was not used.
Training on the A100 cluster
Item | Value
Cluster | 1 × A100-SXM4-40GB (8-GPU node, UP COE HPC)
Objective / optimiser | BCE, smoothing 0.05 · AdamW lr 2e-3, cosine
Epochs / loss | 60 epochs, 26 min · best epoch 36 / 0.167
Pi 5 resource use (both models running)
Item | Value
CPU (runtime) | 12.8% of one core on average, 22.8% at most
RAM | 109 MB runtime · 648 MB of 4 GB for the whole Pi
Temperature | 54.5 °C mean, 57.3 °C max · no throttling
Notes: Wakeword model: data/deliverables/model/runs/bcresnet6 (round 1c). Threshold 0.7335 = lowest with <=1% false positives in every negative category on validation; 2-of-3 rule, 1 s refractory. Wake detect and false-wake numbers come from the class benchmark of 2026-10-03 (202 trials with the wake word, 16 without; 2026-10-02: 199 of 202, 0 of 16). Held-out test: model/runs/bcresnet6/test/test_report.md. Latency 4.8 ms was measured on one server CPU core, not on the Pi. What made the difference (data/deliverables/model/README.md): (1) round 1 trained on 5 TTS voices: validation synthetic 17/27 (one unseen voice, 63%); with 405 Whisper-verified Piper voices 176/194 (91%). (2) short clips were padded with quiet before augmentation, so quiet flanks became a cue; adding background over the whole window cut Qualcomm 'Hey/Hi + word' false accepts from 3.7% to 0.07%. (3) hard-negative mining lowered the threshold to 0.45 and raised streaming false accepts to 17.3/h (vs 6.2/h), so it was not used. Pi resource numbers: class benchmark run 20261002-135144 on the Pi 5 (60 min, 202 trials), runtime process = the full listener with the wakeword + hf_plus command model (data/deliverables/evaluation/20261002-135144/report.md). The 2026-10-03 run is not used for CPU/RAM: there the Pi ran three command models side by side (145 MB).

## Slide 2: ME2 — Hey Delta Command Model
Fixed-vocabulary intent recognition at the edge · no speech-to-text
3 October 2026 · Arvir Jane R. Redondo · Model · Training on A100 · Validation on Raspberry Pi 5
Model
Captured clip · 16 kHz → log-mel 40 × 497 (5 s)
BC-ResNet-6 encoder × 12 blocks · 96 → 192 channels
same trunk as the wakeword model · only the head differs
Intent head · 32-way softmax
Slots in classes, e.g. TIMER_30S
Actuator · bulb, phone, music
Raspberry Pi 5 · 4 GB
Item | Value
Parameters / weights | 0.19 M trainable (191,672) · 1.91 MB ONNX
Validation on the Raspberry Pi 5
Item | Value
Intent / command acc | 84.7% / 84.2% (TTS voices 94.3%, real 74.0%)
False-accept rate | 6.2% (1 of 16 out-of-scope) · misfire 2.2%
Latency p95 / RTF | 72.1 ms inference / 0.012 · reply p95 3.3 s
Runtime | onnxruntime · 1 thread · 109 MB RAM
Training data: HF only vs HF + our data
What differs | HF only → HF + our data
Clips / speakers | 10,682 → 187,480 clips · 315 → 15,052 speakers (17× the clips)
“Not a command” examples | 359 (3%) → 110,015 (59%): other words, speech, noise, cut-off commands
Clips via the Pi microphone | 577 → 3,001, incl. voice-converted copies and room background
Training on the A100 cluster
Item | Value
Cluster | 1 × A100-SXM4-40GB (8-GPU node, UP COE HPC)
Objective / optimiser | cross-entropy, smoothing 0.05 · AdamW 2e-3, cosine
Steps / loss | 22,500 steps × 128 (82 min) · best epoch 43 / 1.05
Benchmark: HF only vs HF + our data
Benchmark (same clips) | HF only → HF + our data
Intent accuracy | 50.5% → 84.7% (balanced cutoff)
Real voices | 28.1% → 74.0%
Commands rejected | 52.7% → 14.0% · non-commands acting 1 of 16 both
Notes: Command model: bcresnet6_hf_plus (data/deliverables/command_classifier/model/runs/bcresnet6_hf_plus), balanced rule: act on the top class only if its probability >= 0.34. Validation = class benchmark run 20261003-075251 on the Pi 5 (202 trials + 16 without wake word, holdout HF da92a79, seed 79276), hf_plus balanced column of data/deliverables/evaluation/benchmark_comparison.md. In that run the Pi ran several command models on every capture; hf_plus balanced was scored with the benchmark's --rescore on the same captures. Reply latency = time to the Pi's first answer in that run. RAM 109 MB is from the one-model run of 2026-10-02. Same captures, cautious rule (0.61): 75.2% intent accuracy, 25.3% rejected, 1.6% misfire, 0 of 16 non-commands acting. 2026-10-02 cautious run: 69.8%. 191,672 trainable parameters; the ONNX file holds 474,512 numbers because it includes the fixed audio front end, see presentation_guidelines.txt. Training loss 1.05 is on augmented clips with label smoothing. Where it fails (not on the slide): false reject 14.0% vs misfire 2.2%; the 4 misfires are opposites (Lower the volume -> VOLUME_UP twice; Stop playing music / Turn off the music -> PLAY_MUSIC); the 1 false accept: 'Start the washing machine.' -> LIGHT_OFF. Rejections: BRIGHTNESS, TEMPERATURE, TIMER, ALARM, PAUSE 3 each. PAUSE 3 of 6, STOP 3 of 6. Training data (data/commands_hf_only.csv vs data/commands_hf_plus.csv, train split): command clips 10,323 vs 77,465; Pi-microphone clips = owner recordings + voice-converted owner clips + room background + owner fragments. Added data vs HF only: same 202 captures, balanced cutoffs (hf_only 0.67, hf_plus 0.34); our added data = owner Pi recordings, public sets (GSC, Fluent Speech Commands, SLURP, Timers and Such), Philippine-accent TTS + voice clones, phrasing variants, non-command speech and noise. Both BC-ResNet-6, same recipe.